## Slide 1: Acetabular Coverage Method
Kyle Miller
Prepared for: Dr. Daisuke Hara and Dr. Scott Banks

## Slide 2: Introduction
The following guide will demonstrate how to calculate the intact ratio according to the following formula:
Intact ratio = Femoral Head WBS – Necrotic WBS
Femoral Head WBS
As of this moment, the program currently outputs WBS areas for each input of a joint track pose (.jtp) inside a .jts

## Slide 3: Step 1: Add Folder to Path
Everything you need is contained in the folder labeled ‘For Daisuke’. Make sure to first add this to path with selected subfolders.

## Slide 4: Step 2: Open and Run GUI_MainWindow.m
This is the only file you will need to open as all the others are referenced and in the path

## Slide 5: Step 3: Upload .stl files
ALWAYS UPLOAD FEMUR FIRST. Browse to your files as shown:

## Slide 6: Note on Camera Controls
Select the far left widget as shown. Once a widget is selected, right click on the window to pull up full camera options.

## Slide 7: Step 4: Transform Models with JTS
Tools -> Transform Model -> Browse to JTS

## Slide 8: Tip for Transform Models
Make sure that the JTS files for both the pelvis and the femur have been truncated to the same length.
Also, make sure that the JTS files match up. I.e. don’t pair a pelvis kinematics file with a femur component

## Slide 9: Step 5: Bind Regions
Tools -> Create Region Object from Model -> Select Model -> Accept

## Slide 10: Step 6: Nearest Neighbor
Tools -> Nearest Neighbor -> Set Region 2

## Slide 11: Step 7: Retrieving Data
Following the Nearest Neighbor Calculation, data will have populated the Command Window at the bottom of Matlab
In this area, browse to find the Surface Area Data the program collected from each frame:

## Slide 12: Tips for Retrieving Data:
If you open the NearestNeighbour_tool.m and comment out line 370 the Command Window will be less populated with data

## Slide 13: Notes on Distances
In the Nearest Neighbor window you may have noticed the following widgets:
This is referenced in the program with these equations: (Units are pixels)